# Text boxes

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

Drawing No:	KP9 Series

#### Panic Button

Drawn:		Chris Moorman

Date:		09/02/09

All dimensions in mm

Do not scale

Description:

Grade 1 Class II

Mini Single End Push Panic Button

Materials:

ABS / Acetal

Metal Key x 2

Temperature Range:

-40oC to +50oC

Tampers:

Stainless Steel

Metal Key Provided inside

Switching Current

500mA Max DC

500mA Max AC

Contact Material:

Rhodium

Voltage Range:

1 – 100v DC

125v AC Max

Colours:

White

Finishes:

Plastic

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

|  | Model |
| --- | --- |
|  |  | KP9 | KP9NT |
| Grade 1 Class II |  | ● | ● |
| Latch |  | ● | ● |
| Non Latch |  | ● | ● |
| Protected Reed |  | ● | ● |
| Tampered |  | ● | - |
| Reed NO |  | ● | ● |
| Reed NC |  | ● | ● |
| Metal Key inside |  | ● | ● |
| Spare Keys to Order |  | ● | ● |  |  |
| 6 Terminals |  | ● | ● |  |  |
| End Knock-out |  | ● | ● |  |  |
| Back Knock-out |  | ● | ● | ● | ● |
| 2 Side Knock-outs |  | ● | ● | ● | ● |
| Recess for Labels |  | ● | ● |  |  |
|  | Length | Width | Height |  |  |
| Dimensions | 67 | 52 | 26mm |  |  |

Fig. 1- KP9 End Push Panic Button