# Text boxes

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Drawing No:	A90

Drawn:		Chris Moorman

Date:		04/09/09

All dimensions in mm

Do not scale

Description:

Grade 1	Class 1

6 Terminal Flush Contact Quick Fit Double Reed

Operating Gap:

25-30mm (Approx)

Materials:

High Impact Polystyrene

Stainless Steel Plate

Magnet:

Ferrite or Alnico V

Contact Material:

Rhodium

Voltage Range:

1 – 100v DC

125v AC Max

Switching Current

500mA Max DC

500mA Max AC

Temperature Range:

-40oC to +50oC

Colours:

White (No Suffix)

Brown (Suffix B)

Fixing Screws Provided

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.