# Text boxes

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

Drawing No:	ZO1-Z20 Final

Exit Switches

Drawn:		Chris Moorman

Date:		04/09/09

All dimensions in mm

Do not scale

Description:

Grade 2 & 3 Class III

Final Exit Set Switch

Materials:

Body and Cover Plate - ABS

Diaphragm - EVA

Temperature Range:

-40oC to +125oC

Reed:

Sealed Magnetic Reed Switch

Switching Current

500mA Max DC

Voltage Range:

200v DC Max

Colours:

ZO1 – ZO2 – White

Z20 – White,  Z20B - Black

Fittings:

Wire Clamping Terminals

Concealed Fixing Screws

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

|  | Model |
| --- | --- |
|  | Z01 | Z02 | Z20 | Z20B |
| Grade 2 Class III | ● | ● | - | - |
| Grade 3 Class III | - | - | ● | ● | ● |
| Weatherproof casing | ● | ● | ● | ● |
| Sealed Reed Switch | ● | ● | - | - |
| ABS Body | ● | ● | - | - |
| EVA Diaphragm | ● | ● | - | - |
| Fitted Resistor | - | ● | - | - |
| Ind. Terminals | - | ● | - | - |
| LED Green | - | ● | - | - |
| LED Red | - | ● | - | - |
| Sound Pressure 90DBA/30cm | ● | ● | - | - |
| Z01-Z02 | Length | Width | Height |
| Dimensions Fascia | 45 | 25 | 6mm |
| Dimensions Body | 45 | 27 | 15.5mm |
| Micro-Switch | - | - | ● | ● |
| Tampered | - | - | - | - |
| Flush Mounted | ● | ● | - | - |
| Surface Mounted | - | - | ● | ● |
| Concealed Fixings | - | - | ● | ● |
| Z20-Z20B | Length | Width | Height |
| Dimensions | 54 | 35 | 21mm |

Fig. 4 – Z20B Final Exit Set Switch

Fig. 1 - Z01 Flush Final Exit Set Switch

Fig. 2 - Z02 Flush Final Exit Set Switch

Fig. 3 – Z20 Final Exit Set Switch