The PDH10A4K72K2 is an angle contact sealed against outside attack, complete with armoured cable sleeving. Wire selection enables the resistors required for your installation.

INSTALLATION

For a no resistor setup, connect the RED and YELLOW wires to the zone.

For alarm resistor only, twist the RED and BLACK wires together and connect to one end of the zone. The YELLOW wire should be connected to the other end of the zone.

For EOL resistor only, connect the RED and BLUE wires to the zone.

If both resistors are to be used, twist the RED and BLACK wires together and connect to one end of the zone. Connect the BLUE wire to the other end of the zone.

Tamper wires are both WHITE. Connect these to a common tamper in the panel.

The wiring diagram below visualises these instructions.

WIRING DIAGRAM

# Text boxes

REED

4k7 ALARM

2k2 EOL

RED

BLACK

YELLOW

BLUE

WHITE

WHITE