# Text boxes

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Drawing No:	PDA40 +RESISTORS

Drawn:		Chris Moorman

Date:		04/09/09

All dimensions in mm

Do not scale

Description:

Grade 2	Class III

5 Terminal Flush Contact Single Reed, pre-fitted pre-set resistors.

Operating Gap:

14mm (Approx)

Materials:

High Impact Polystyrene

Magnet:

Ferrite or Alnico V

Contact Material:

Rhodium

Voltage Range:

1 – 100v DC

125v AC Max

Switching Current

500mA Max DC

500mA Max AC

Temperature Range:

-40oC to +50oC

Resistor Combinations:

See Inset Panel

Call for options.

Colours:

White (No Suffix)

Brown (Suffix B)

Fixing Screws Provided

Sealed against outside attack.

Can be used with just the reed switch and no resistors – connect the yellow wire and the red wire.

To include 1 resistor, twist the red & white wires together to link, then connect the yellow wire.

To include 2 resistors, twist the red & white wires together to link then connect the green wire.

Black and blue wires are the tamper loop.

The magnet side needs to be fitted approx. 14mm away from the reed side.