# Text boxes

REED

(DOOR OPEN)

TAMPER

SWITCH

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

Description:

Grade 2	Class II

4 + 2 Terminal Contact

Single Normally-Open Reed TACTILE Switch Tamper

Operating Gap:

35mm (Approx)

Materials:

ABS

Magnet:

Ferrite

Contact Material:

Rhodium

Voltage Range:

15v DC Max

Switching Current

250mA Max DC

Temperature Range:

-40oC to +50oC

Colours:

White (No Suffix)

Brown (Suffix B)

Fixing Screws Provided

All dimensions in mm

Do not scale

## Knight

### Fire & Security Products Ltd

mailto:info@knightfireandsecurity.com

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

Drawing No:	D75NO

Drawn:			Chris Moorman

Date:			20/07/09

	Wire to the 2 terminals to the right of the tactile switch marked Tamp for the tamper.

	Wire to the 2 terminals extreme right, to connect the alarm.

	The 2 left terminals are spare.

The operating gap is approx. 35mm.

Note : Mounting on metal surfaces, that can be magnetised, can reduce the functionality of this product. If in doubt contact us for more information.