# Text boxes

( Screw the unit base to mounting surface.

( Connect your alarm circuit wires to the PA contacts. This

will create the circuit. Once the button is pressed in the circuit

will be broken.

( Attach your tamper wires to the tamper terminals. If the lid is

removed the tamper will activate.

Other terminals are spare.

( Carefully fit the lid to the central post on the base.

( Ensure no snagging occurs.

( Operation:- Push Side button inwards. The microswitch will only operate when both buttons are pushed simultaneously.

( Reset :- by using the reset key (supplied)

|  | Model |
| --- | --- |
|  | PA2S |
| Grade 3 Class II |  | ● |  |
| Microswitch Activation |  | ● |  |
| Tactile Switch Tamper |  | ● |  |
| Metal Reset Key |  | ● |  |
| Spare Keys to Order |  | ● |  |
| 5 Terminals |  | ● |  |
| End Knock-out |  | ● |  |
| Back Knock-out |  | ● |  |
| 2 Side Knock-outs |  | ● |  |
| Finishes | Plastic | Brass | St/Steel |
|  | PA2SBW | PA2SBR | PA2SSR |
| Installation Instructions | ● | ● | ● |
|  | Length | Width | Height |
| Dimensions | 80 | 62 | 28mm |
| Selectable Resistor Values | EOL | Alarm |  |
| Ademco, Honeywell | 1K | 1K |  |
| Castle, Menvier, Pyronix, Texecom, Scantronic | 2K2 | 4K7 |  |
| Aritech | 4k7 | 4K7 |  |
| DSC | 5K6 | 5K6 |  |
| Gardtec | 4K7 | 6K8 |  |
| Guardall | 8K2 | 8K2 |  |

Description:

Grade 3 Class II

Double Side Push Panic Button. With Selectable Resistors

Manufactured to BS EN50131

Materials:

ABS

Temperature Range:

-40oC to +50oC

Tampers:

Tactile Switch Tamper

###### Switching Current:

500mA Max DC

Voltage Range:

15v DC Max

Body Colours:

White, PA2SWR

Black (S/Steel Cover) PA2SSR

Grey if requested

Surface Finishes:

Plastic PA2SWR

Brass PA2SBR

Stainless Steel. PA2SSR

All dimensions in mm

Do not scale

Drawing No:	PA2S Range

#### Panic Buttons

Drawn:		Chris Moorman

Date:		11/03/10

## Knight

### Fire & Security Products Ltd

mailto:info@knightfireandsecurity.com

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

Fig. 1	PA2S

Double Side Push Panic Button