Installation

Fix the units to the mounting surfaces using the fixing holes provided.  When fitting to metal surfaces we recommend the use of SPA-SS, Plastic Spacer to reduce magnetic interference.

Align the contact parts with the MARKER as shown opposite.

The MAKE DISTANCE in this alignment is approximately 10mm and the BREAK DISTANCE is approximately 20mm.

Align the contact parts with the MARKER as shown opposite.

The MAKE DISTANCE in this alignment is approximately 12mm and the BREAK DISTANCE is approximately 20mm.

### Operation

### Select the appropriate wiring format and/or resistor values (see tables below).

Single Zone

| PANEL | EOL | ALARM | Wiring to panel |
| --- | --- | --- | --- |
|  |  |  | Connection 1 | Connection 2 |
| Honeywell / Ademco | 1k | 1k | BLACK | LINK GREEN to BLUE |
| Europlex (3GS & Aplex) | 2k2 | 2k2 | LINK RED to YELLOW | LINK GREEN to BROWN |
| Castle, Menvier, Pyronix (PCX), Scantronic, Texecom (Premier) | 2k2 | 4k7 | LINK RED to YELLOW | LINK GREEN to WHITE |
| Aritech, Pyronix (Matrix) | 4k7 | 4k7 | YELLOW | LINK GREEN to WHITE |
| Gardtec | 4k7 | 6k8 | YELLOW | GREEN |
| Guardall NOTE: link Blue and White | 8k2 | 8k2 | RED | GREEN |

NOTE : Where two wires are indicated they are to be connected together.

Shared Zone

NOTE : New panels are being introduced regularly. If using on a shared zone, where possible please disable masking and check fault/tamper values against the table to ensure that the operation of both contacts on the zone doesn’t lead to a fault/tamper on the panel.

Check that this is acceptable for your panel

| PANEL | EOL | ALARM | contact 1 wiring | contact 2 wiring |
| --- | --- | --- | --- | --- |
| Honeywell, Ademco | 1k | 1k | Orange | Green + Blue | Black | Green + Blue |
| Europlex (3GS & Aplex) NOTE : link Blue and White | 2k2 | 4k4 | Orange | Green +Brown | Red + Yellow | Green +Brown |
| Castle, Pyronix (PCX), Texecom (Premier) | 2k2 | 4k7 | Orange | Green + White | Red + Yellow | Green + White |
| Aritech, Pyronix (Matrix) | 4k7 | 4k7 | Orange | Green + White | Yellow | Green + White |
| Gardtec | 4k7 | 6k8 | Orange | Green | Yellow | Green |
| Guardall / Menvier/Scantronic | See wiring diagrams |

For example : Honeywell / Ademco

Guardall : Note the different wiring method for the Guardall panel.

(Menvier/Scantronic : Note the different wiring method for the Cooper panel

Ensure that unused wires and any trimmed wires cannot short out to the contact body or any other connections.

The following table gives the resistance for each situation for several panels :-

| PANEL | Contact 1 & 2 SET (closed) | Contact 1 OPEN | Contact 2 OPEN | Contact 1 & 2 OPEN |
| --- | --- | --- | --- | --- |
| Honeywell / Ademco | 1k | 2k | 2k | 3k |
| Europlex (3GS & Aplex) | 2k2 | 4k0 | 4k0 | 5k8 |
| Castle, Pyronix (PCX), Texecom (Premier) | 2k2 | 6k9 | 6k9 | 11k6 |
| Aritech, Pyronix (Matrix) | 4k7 | 9k4 | 9k4 | 14k1 |
| Gardtec | 4k7 | 11k5 | 11k5 | 18k3 |
| Guardall | 4k1 | 7k5 | 7k5 | 8k6 |
| Menvier/Scantronic | 2k | 6k | 6k | 7k6 |

# Text boxes

Knight Fire & Security Products Ltd

Unit 84,

Seawall Road Industrial Estate

Tremorfa, Cardiff CF24 5TH

TEL : 02920 488129

Fax : 02920 489132

www.knightfireandsecurity.com

SURFACE CONTACT with Selectable Resistors

Part Code : YE50

Security Grade 3 Environmental Class 3

Manufactured to BS EN 50131-2-6