# Text boxes

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

Drawing No:	YE50

Drawn:			Chris Moorman

Date:			17/05/10

All dimensions in mm

Do not scale

Description:

Grade 3 Class III

G3 Potted Surface Contact, Selectable Resistors

Operating Gap:

20mm (Approx)

Materials:

High Impact Polystyrene

1 metre 8 core cable

Magnet:

Ferrite or Alnico V

Contact Material:

Rhodium

Voltage Range:

12v DC Max

Switching Current:

500mA Max DC

Temperature Range:

-40°C to +50°C

Resistor Combinations:

See Inset Panels

Colours:

White (No Suffix)

Brown (Suffix B)

Fixing Screws Provided

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

Description	The YE50 is a universal fully sealed Surface Contact with magnetic shielding.  It meets all of the necessary requirements for magnetic contacts permitting it to be used within Grade 3 installations.  The contact has installer selectable End of Line (EOL) and alarm contact bypass resistors, and benefits from the option of a second device connected in series.

Installation		Fix the contact plate to the prepared mounting surfaces using the fixing holes provided.  Feed the cable from the contact, and wire into the appropriate terminal blocks. Select the appropriate wiring format and resistor values (see tables alongside).  Ensure that unused wires and any trimmed wires cannot short out to any other connections.  Only two connections are made to the control panel alarm circuit and this provides both the alarm and tamper information.

##### Operating Gap

According to orientation the make distance is approximately 10-12mm, and the break distance is approximately 20mm.

Note: Mounting on metal surfaces reduces the functionality, according to the metal type and thickness.  When fitting to metal surfaces we recommend the use of SPA-SS, Plastic Spacer to reduce magnetic interference.

Wiring:- 	The YE50 is only suitable for fully supervised (EOL) formats. Use the appropriate wires colours and combinations to achieve the necessary end of line and alarm bypass resistor values for single zone or shared zone operation, (see tables alongside).

###### Wiring 2 x YE50 Contacts in Series