# Text boxes

Description:

Grade 2 Class II

Surface Contact Reed, selectable pre-set resistor jumpers.  Tactile switch tamper.

Operating Gap:

25-35mm (Approx.)

Materials:

High Impact Polystyrene

Magnet:

Ferrite or Alnico V

Contact Material:

Rhodium

Voltage Range:

15v DC Max

#### Switching Current

500mA Max DC

500mA Max AC

Temperature Range:

-40oC to +50oC

Resistor Combinations:

See Inset Panel

Colours:

White (No Suffix)

Brown (Suffix B)

Fixings:

Mounting & Fixing Screws Provided

Description:  The D75 multi is a surface mount contact with integral tamper switch.  It can be wired in traditional or fully supervised (EOL) formats.  The contact has installer selectable End of Line (EOL) and alarm contact bypass resistors, and benefits from the option of a second device connected in series.

Installation:  Fix the contact to the mounting surfaces using the screws provided.  For optimum performance the centres of the reed and magnet should be aligned.

Operation:  The contact will operate with a gap of 25-35mm between the magnet and reed.

Wiring:-

Traditional:  (4 Wire) – Ensure no jumpers are fitted.  Use all four terminals as marked.

Supervised: (EOL):   – Fit the appropriate jumpers for the control panel (See Table).  Connect the loop wires to the terminals marked (

Note this contact meets the requirements of BS EN 50131-2-6 g2.

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

## Knight

### Fire & Security Products Ltd

### mailto:info@knightfireandsecurity.com

Drawing No:	D75 multi

Drawn:		R.Maidment

Date:		20 Sept 2012

All units in mm

Do not scale

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

D75 multi Shared Zone Wiring