# Knight Fire & Security Products Ltd

Unit 84, Seawall Road Industrial Estate

Tremorfa, Cardiff CF24 5TH

Tel:		00 44 29 20 48 81 29

### Fax: 	00 44 29 20 48 91 32

mailto:info@knightfireandsecurity.com

### Part Code: KP1S		Security Grade 1		Environmental Class 2		With Lid Tamper & Reed

(	Screw the unit base to mounting surface.

(Connect your alarm circuit wires to the reed terminals T1 and T2. This will create the circuit. Once the button is pressed in the circuit will be broken.

(Attach your tamper wires to terminals T3 and T4. If the lid is removed the tamper will activate.

Other terminals are spare.

(Carefully fit the lid to the central post on the base.

(Ensure no snagging occurs.

(Operation:- Push End button inwards.

(Reset :- by using the reset key (supplied)

# Text boxes

INSTALLATION INSTRUCTIONS

SINGLE PUSH PANIC BUTTON