# Text boxes

( Screw the unit base to mounting surface.

( Connect your panel wires to the terminal block as per the instructions, dependant on whether you want 4-wire, supervised or 2 in series.

( Select your resistors by moving the jumpers in line with instructions. Select Multi if you are fitting more than 1 PA to a zone

( Carefully fit the lid to the central post on the base

( Ensure no snagging occurs.

( Operation:- Push End button inwards. The microswitch will only operate when both buttons are pushed simultaneously.

( Reset :- by using the reset key (supplied)

|  | Model |
| --- | --- |
|  | PA2E |
| Grade 3 Class II |  | ● |  |
| Microswitch Activation |  | ● |  |
| Tactile Switch Tamper |  | ● |  |
| Metal Reset Key |  | ● |  |
| Spare Keys to Order |  | ● |  |
| 5 Terminals |  | ● |  |
| End Knock-out |  | ● |  |
| Back Knock-out |  | ● |  |
| 2 Side Knock-outs |  | ● |  |
| Finishes | Plastic | Brass | St/Steel |
|  | PA2EBW | PA2EBR | PA2ESR |
| Installation Instructions | ● | ● | ● |
|  | Length | Width | Height |
| Dimensions | 80 | 62 | 28mm |
| Selectable Resistor Values | EOL | Alarm |  |
| Ademco, Honeywell | 1K | 1K |  |
| Castle, Menvier, Pyronix, Texecom, Scantronic | 2K2 | 4K7 |  |
| Aritech | 4k7 | 4K7 |  |
| DSC | 5K6 | 5K6 |  |
| Gardtec | 4K7 | 6K8 |  |
| Guardall | 8K2 | 8K2 |  |

Description:

Grade 3 Class II

Double End Push Panic Button. With Selectable Resistors

Manufactured to BS EN50131

Materials:

ABS

Temperature Range:

-40oC to +50oC

Tampers:

Tactile Switch Tamper

###### Switching Current:

500mA Max DC

Voltage Range:

15v DC Max

Body Colours:

White, PA2EWR

Black (S/Steel Cover) PA2ESR

Grey if requested

Surface Finishes:

Plastic PA2EWR

Brass PA2EBR

Stainless Steel. PA2ESR

All dimensions in mm

Do not scale

Drawing No:	PA2E Range

#### Panic Buttons

Drawn:		Chris Moorman

Date:		11/03/10

## Knight

### Fire & Security Products Ltd

Unit 84 Seawall Road Ind. Estate

Cardiff  UK CF24 5TH

Tel:	0 (00 44) 29 20 48 81 29

Fax:	0 (00 44) 29 20 48 91 32

© Knight Fire & Security Products Ltd

All cases of ™ Infringement will be pursued.

Selectable      Resistors Here

PA2 Panic Button Inside

Multi contact jumper

Connect Panel Wires Here