# Text boxes

SINGLE ZONE : JUMPER SETTINGS

| Control Panel | Value | Jumper |
| --- | --- | --- |
|  | EOL | Alarm | EOL | Alarm |
| Honeywell (Ademco/Microtech) | 1k | 1k | A | 1 |
| Cooper (Scantronic, Menvier) Texecom, Pyronix, Castle | 2k2 | 4k7 | BC | 2 |
| Aritech | 4k7 | 4k7 | C | 2 |
| Guardtec | 4k7 | 6k8 | C | 3 |
| Guardall | 4k1 | 4k1 | B | 2 & 4 |
| DSC | 5k6 | 5k6 | D | 3 & 4 |
| Europlex | 2k2 | 2k2 | BC | 5 |

Operation:- Push Side buttons inwards. The microswitch will only operate when both buttons are pushed simultaneously.

### Reset :- by using the reset key (supplied)

Wiring

Traditional (4 Wire) – Ensure no jumpers are fitted.  Use all four terminals as marked.

Supervised (EOL) – Fit the appropriate jumpers for the control panel (See Table).  Connect the loop wires to the terminals marked (. Fit Jumpers to the multi-contact link W to X and Y to Z.

Other – Some applications may not require both resistors.  In these cases fit jumper(s) in EOL or Alarm position as appropriate

JP3

Contact 1

Fit EOL jumper.

Fit ALARM jumper.

Change multiple contact jumper as shown.

Contact 2

Do NOT fit EOL jumper.

Do NOT fit ALARM jumper.

Change multiple connector jumper as shown.

Tamper

Alarm

Zone wire

Zone wire

JP3

4

34

2

1

Tamper

Alarm

W

Y

Contact 1

Fit EOL jumper.

Fit ALARM jumper.

Change multiple contact jumper as shown.

# Wiring Two PA2EWR Contacts in Series (Shared Zone)

Select the appropriate EOL and Alarm links for contact 1. Do not fit any links for contact 2. Link the Multi-contact jumper W to Y for contact 1 and Z to X for contact 2.

SINGLE ZONE : JUMPER SETTINGS

| Control Panel | Value | Jumper |
| --- | --- | --- |
|  | EOL | Alarm | EOL | Alarm |
| Honeywell (Ademco/Microtech) | 1k | 1k | A | 1 |
| Cooper (Scantronic, Menvier) Texecom, Pyronix, Castle | 2k2 | 4k7 | BC | 2 |
| Aritech | 4k7 | 4k7 | C | 2 |
| Guardtec | 4k7 | 6k8 | C | 3 |
| Guardall | 4k1 | 4k1 | B | 2 & 4 |
| DSC | 5k6 | 5k6 | D | 3 & 4 |
| Europlex | 2k2 | 2k2 | BC | 5 |

1

2

Z

X

Operation:- Push Side buttons inwards. The microswitch will only operate when both buttons are pushed simultaneously.

### Reset :- by using the reset key (supplied)

Wiring

Traditional (4 Wire) – Ensure no jumpers are fitted.  Use all four terminals as marked.

Supervised (EOL) – Fit the appropriate jumpers for the control panel (See Table).  Connect the loop wires to the terminals marked (. Fit Jumpers to the multi-contact link W to X and Y to Z.

Other – Some applications may not require both resistors.  In these cases fit jumper(s) in EOL or Alarm position as appropriate

34

4

Knight Fire & Security Products Ltd

## Unit 84, Seawall Road Industrial Estate

## Tremorfa, Cardiff CF24 5TH

### Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

4

Zone wire

Contact 2

Do NOT fit EOL jumper.

Do NOT fit ALARM jumper.

Change multiple connector jumper as shown.

Contact 1

Fit EOL jumper.

Fit ALARM jumper.

Change multiple contact jumper as shown.

# Wiring Two PA2EWR Contacts in Series (Shared Zone)

Select the appropriate EOL and Alarm links for contact 1. Do not fit any links for contact 2. Link the Multi-contact jumper W to Y for contact 1 and Z to X for contact 2.

SINGLE ZONE : JUMPER SETTINGS

| Control Panel | Value | Jumper |
| --- | --- | --- |
|  | EOL | Alarm | EOL | Alarm |
| Honeywell (Ademco/Microtech) | 1k | 1k | A | 1 |
| Cooper (Scantronic, Menvier) Texecom, Pyronix, Castle | 2k2 | 4k7 | BC | 2 |
| Aritech | 4k7 | 4k7 | C | 2 |
| Guardtec | 4k7 | 6k8 | C | 3 |
| Guardall | 4k1 | 4k1 | B | 2 & 4 |
| DSC | 5k6 | 5k6 | D | 3 & 4 |
| Europlex | 2k2 | 2k2 | BC | 5 |

1

2

34

Knight Fire & Security Products Ltd

## Unit 84, Seawall Road Industrial Estate

## Tremorfa, Cardiff CF24 5TH

### Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

Double Push Panic Button

Part Code : PA2EWR

Security Grade 3 Environmental Class 2

Manufactured to BS EN50131-2-6

Operation:- Push Side buttons inwards. The microswitch will only operate when both buttons are pushed simultaneously.

### Reset :- by using the reset key (supplied)

Wiring

Traditional (4 Wire) – Ensure no jumpers are fitted.  Use all four terminals as marked.

Supervised (EOL) – Fit the appropriate jumpers for the control panel (See Table).  Connect the loop wires to the terminals marked (. Fit Jumpers to the multi-contact link W to X and Y to Z.

Other – Some applications may not require both resistors.  In these cases fit jumper(s) in EOL or Alarm position as appropriate

4

Z

X

Z

X

Y

Y

W

Alarm

Y

W

Alarm

Z

X

Y

W

Alarm

Tamper

Z

X

Y

W

Alarm

1

2

W

Z

# Wiring Two PA2EWR Contacts in Series (Shared Zone)

Select the appropriate EOL and Alarm links for contact 1. Do not fit any links for contact 2. Link the Multi-contact jumper W to Y for contact 1 and Z to X for contact 2.

Knight Fire & Security Products Ltd

## Unit 84, Seawall Road Industrial Estate

## Tremorfa, Cardiff CF24 5TH

### Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

Double Push Panic Button

Part Code : PA2EWR

Security Grade 3 Environmental Class 2

Manufactured to BS EN50131-2-6

Operation:- Push Side buttons inwards. The microswitch will only operate when both buttons are pushed simultaneously.

### Reset :- by using the reset key (supplied)

Wiring

Traditional (4 Wire) – Ensure no jumpers are fitted.  Use all four terminals as marked.

Supervised (EOL) – Fit the appropriate jumpers for the control panel (See Table).  Connect the loop wires to the terminals marked (. Fit Jumpers to the multi-contact link W to X and Y to Z.

Other – Some applications may not require both resistors.  In these cases fit jumper(s) in EOL or Alarm position as appropriate

Knight Fire & Security Products Ltd

## Unit 84, Seawall Road Industrial Estate

## Tremorfa, Cardiff CF24 5TH

### Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

Double Push Panic Button

Part Code : PA2EWR

Security Grade 3 Environmental Class 2

Manufactured to BS EN50131-2-6

1

2

34

4

Z

X

Y

W

Alarm

Z

X

Y

W

Alarm

Double Push Panic Button

Part Code : PA2EWR

Security Grade 3 Environmental Class 2

Manufactured to BS EN50131-2-6

Tamper

Tamper

JP3

JP3

Tamper

JP3

Zone wire

1

2

34

4

Zone wire

Contact 2

Do NOT fit EOL jumper.

Do NOT fit ALARM jumper.

Change multiple connector jumper as shown.

Tamper

JP3

Zone wire

1

2

34

X

34

4

JP3

Tamper

JP3

Zone wire

1

2

34

4

Zone wire

Contact 2

Do NOT fit EOL jumper.

Do NOT fit ALARM jumper.

Change multiple connector jumper as shown.

Contact 1

Fit EOL jumper.

Fit ALARM jumper.

Change multiple contact jumper as shown.

# Wiring Two PA2EWR Contacts in Series (Shared Zone)

Select the appropriate EOL and Alarm links for contact 1. Do not fit any links for contact 2. Link the Multi-contact jumper W to Y for contact 1 and Z to X for contact 2.

SINGLE ZONE : JUMPER SETTINGS

| Control Panel | Value | Jumper |
| --- | --- | --- |
|  | EOL | Alarm | EOL | Alarm |
| Honeywell (Ademco/Microtech) | 1k | 1k | A | 1 |
| Cooper (Scantronic, Menvier) Texecom, Pyronix, Castle | 2k2 | 4k7 | BC | 2 |
| Aritech | 4k7 | 4k7 | C | 2 |
| Guardtec | 4k7 | 6k8 | C | 3 |
| Guardall | 4k1 | 4k1 | B | 2 & 4 |
| DSC | 5k6 | 5k6 | D | 3 & 4 |
| Europlex | 2k2 | 2k2 | BC | 5 |