# Knight Fire & Security Products Ltd

Unit 84, Seawall Road Industrial Estate

Tremorfa, Cardiff CF24 5TH

Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

Description:

The Z30 is a tough stainless steel finish, final exit switch with integral buzzer and 8

core cable, for use with all main UK Panels. It is a vandal resistant flush mounting

button supplied with a mounting plate. It can be used without Face Plate if space is

limited and is intended to be wired in a fully supervised (EOL) format. It benefits

from installer selection of End of Line and Alarm contact bypass resistors,

permitting use within Grade 3 installations.

Installation

Drill a 23mm hole, 30mm deep for both the barrel and retaining nut. Rebate an area 50 x 30mm for the fascia. Alternatively if the face plate is not used

drill a 19mm hole.

Operation

The Z30 is a normally open device, closing upon button activation.

Wiring The Z30 is only suitable for use with systems using supervised (EOL) wiring – Use the appropriate colour wires to achieve the necessary end of line and alarm bypass resistor values for the Control Panel (see table on right). Only two connections are made to the Control Panel alarm circuit, and this provides both alarm and tamper information. Two connections are provided for the buzzer. These should be connected to a 12v supply.

Activation The exit switch will operate on pressing once, (the buzzer will sound for approximately 30 seconds.)

# Knight Fire & Security Products Ltd

Unit 84, Seawall Road Industrial Estate

Tremorfa, Cardiff CF24 5TH

Tel:	029 2048 8129

### Fax:	029 2048 9132

www.knightfireandsecurity.com

Description:

The Z30 is a tough stainless steel finish, final exit switch with integral buzzer and 8

core cable, for use with all main UK Panels. It is a vandal resistant flush mounting

button supplied with a mounting plate. It can be used without Face Plate if space is

limited and is intended to be wired in a fully supervised (EOL) format. It benefits

from installer selection of End of Line and Alarm contact bypass resistors,

permitting use within Grade 3 installations.

Installation

Drill a 23mm hole, 30mm deep for both the barrel and retaining nut. Rebate an area 50 x 30mm for the fascia. Alternatively if the face plate is not used

drill a 19mm hole.

Operation

The Z30 is a normally open device, closing upon button activation.

Wiring The Z30 is only suitable for use with systems using supervised (EOL) wiring – Use the appropriate colour wires to achieve the necessary end of line and alarm bypass resistor values for the Control Panel (see table on right). Only two connections are made to the Control Panel alarm circuit, and this provides both alarm and tamper information. Two connections are provided for the buzzer. These should be connected to a 12v supply.

Activation The exit switch will operate on pressing once, (the buzzer will sound for approximately 30 seconds.)

# Text boxes

#### Flush Final Exit Switch with Selectable Resistors

##### Part Code: Z30

Security Grade 3	Environmental Class 3

Manufactured to BS EN50131

#### Flush Final Exit Switch with Selectable Resistors

##### Part Code: Z30

Security Grade 3	Environmental Class 3

Manufactured to BS EN50131